## Slide 1: LTM-EOPS version 10

## Slide 2: New Vamma 12 (2019): Calculate green certificate contribution
Increased power and capacity:
+ 128 MW
+ 500 m3/s
Upgraded Vamma station (total):
344 MW
1480 m3/s
Expected increase of 230 GWh/year

## Slide 4: Yearly inflow trend curve
Yearly inflow Solbergfoss (365-day average)
Mm3/year

## Slide 5
EOPS version 9:
Simulated average production increase in Vamma:
Period: GWh
1981 – 2010 192
1991 – 2010 195
1998 – 2017 234 (our proposal)
2008 – 2017 246
Problem: NVE *) only accepted 1981 - 2010 as simulation period
*) The Norwegian Energy Regulatory Authority

## Slide 6: What about LTM-EOPS version 10 and daily inflow values?
Improved flow description gives more value of increased capacity
Max. Vamma 1 - 11
Max. Vamma 1 - 12

## Slide 7: Simulated increase with EOPS version 10: 1981 – 2010 239 GWh
NVE accepted the use of EOPS version 10 and 239 GWh were added to our list of green certificates!

## Slide 8: Other usage of EOPS v. 10: Revision and breakdown analysis Data initiation for ProdRisk New LtmSystem.xml file makes it easier to skip DOS.

## Slide 9: Examples:
Breakdown analyses:
Post-simulation calculation per aggregate
Split station production according to pre-defined upload table
Data from file: revisjon.res
EOPS: Find optimum period for revision.
ProdRisk: Run scenarios at given period with and without revision
for better accuracy.

## Slide 10: Other available improvement: Part of flow is included in water-value calculation Better reservoir damping at high levels
Average reservoir 9 vs 10
GWh/week
Reservoir version 10 (average 1051 GWh)
GWh/week

## Slide 11: Working on cloud solution for EMPS / ProdRisk / EOPS + Thema

## Slide 12: Cloud solutions give new possibilities and a lot of new challenges:
EMPS
EOPS
Thema
ProdRisk
FDM
NordPool
Montel
ENTSO-E
- - - - -
SMG
HBV-model
NVE
Blob Storage
Docker Container
C# Python SQL
XML, Javascript
Razor, Blazor
HDF5 format
Web Server / Client
Fire walls
API, Services